SECTION 10100

VISUAL DISPLAY BOARDS

Display hidden notes to specifier. (Don't know how? Click Here)

** NOTE TO SPECIFIER **  EverWhite; Visual Display Boards.
 .
 This section is based on the products of EverWhite, which is located at:
    W158 N9332 Nor-X-Way Ave., Menomonee Falls, WI 53051.
    Tel:  (800) 824-1482.
    Fax: (262) 250-7176.
    Email: inquiry@everwhiteboards.com.
    Web: www.everwhiteboards.com
 .
 Achieving the ultimate in finishing touches is easy with EverWhite, the only dry erase board with a lifetime guarantee against ghosting and staining. Unlike all other dry erase surfaces available, EverWhite will stay bright white thus helping you to achieve the essence of your design. Also, with so many product options, framing types, and colors, EverWhite is easy to spec, easy to install and essentially easy to include in any project.
 .

GENERAL

SECTION INCLUDES

** NOTE TO SPECIFIER **  Delete items below not required for project.

Visual Display Boards.

Bulletin Boards.

Display Board Accessories.

RELATED SECTIONS

** NOTE TO SPECIFIER **  Delete any sections below not relevant to this project; add others as required.

Section 06100 - Rough Carpentry: Wall Framing and Blocking.

Section 05100 - Structural Metal Framing: Wall Framing and Blocking.

Section 09200 - Plaster and Gypsum Board: Wall finishes prepared to receive boards.

REFERENCES

A.	ASTM E 84 - Standard Test Method for Surface Burning Characteristics for Building Materials.

SUBMITTALS

A.       Submit under provisions of Section 01300.

Product Data:  Manufacturer's data sheets on each product to be used, including:

Preparation instructions and recommendations.

Storage and handling requirements and recommendations.

Installation methods.

Shop Drawings: Submit manufacturer's standard drawings detailing plan and section views for each product specified.

** NOTE TO SPECIFIER **  Delete selection samples if colors have already been selected.

Selection Samples:  For each finished product specified, complete sets of samples representing manufacturer's full range of available colors and patterns are available upon request.

QUALITY ASSURANCE

Manufacturer Qualifications:   All primary products specified in this section will be provided by a single manufacturer with a minimum of ten (10) years experience.

Regulatory Requirements: Conform to applicable code for flame/smoke ratings in bulletin boards in accordance with ASTM E84.

DELIVERY, STORAGE, AND HANDLING

After opening and inspecting boards for damage, return them to their original crates or cartons for storage and do not uncrate until boards are to be installed.

When uncrated, do not allow boards to lean at an angle against a wall or other objects, or to lie on the floor for any length of time.

Store boards in as close to a vertical position as possible.

Storage and Protection: Store materials protected from exposure to harmful weather conditions and at temperature and humidity conditions recommended by manufacturer

Store and dispose of hazardous materials, and materials used with hazardous materials, in accordance with requirements of local authorities having jurisdiction.

PROJECT CONDITIONS

Maintain environmental conditions (temperature, humidity, and ventilation) within limits recommended by manufacturer for optimum results.  Do not install products under environmental conditions outside manufacturer's absolute limits.

EverWhite products are designed to be installation-ready, however, installation and the installation environment are out of EverWhite’s control and therefore installation is not warranted by EverWhite in any circumstance.

WARRANTY

The warranty is only valid for the original purchasing entity and covers replacement of defective product but does not include the cost of removal or reinstallation.

Warranty for Laminated Face Sheet: Upon request, provide to owner or owner's representative an executed copy of the Manufacturer's standard warranty in which the manufacturer agrees to repair or replace laminated face sheets that fail in material or workmanship for a period of one year from the date of purchase.  Seller’s sole obligation under this limited warranty would be a refund of the purchase price, subject to EverWhite’s Prorated Depreciation Schedule.

Failures are limited to surfaces that exhibit ghosting or staining. All EverWhite dry erase surfaces are guaranteed against ghosting and staining for the lifetime of the building.  Seller’s sole obligation under this limited warranty would be a refund of the purchase price, subject to EverWhite’s Prorated Depreciation Schedule.

PRODUCTS

MANUFACTURERS

Acceptable Manufacturer:  EverWhite, which is located at: 1480 Independence Ave, Hartford, WI, 53027; Toll Free Tel: 800-355-7319; Fax: 262-250-7176; Email: sales@everwhiteboards.com; Web: www.everwhiteboards.com.

** NOTE TO SPECIFIER **  Delete one of the following two paragraphs; coordinate with requirements of Division 1 section on product options and substitutions.

Substitutions:  Not permitted.

Requests for substitutions will be considered in accordance with provisions of Section 01600.

DISPLAY BOARDS

** NOTE TO SPECIFIER **  Select Display Board Type.  Delete one of the next two paragraphs and modify the included text as instructed.  Delete both if independent Dry Erase Boards are not specified.

Magnetic Dry Erase Board: Balanced, high-pressure, factory-laminated dry erase board assembly of 3-ply construction consisting of backing sheet, core material, and a laminated 24-gauge steel face sheet with durable gloss finish highly resistant to ghosting and staining.

Face Sheet: Laminated 24 gauge steel sheet.

Color: White.

Core Material: 1/2 inch (12mm) thick hexacomb material.

Backing Sheet: 0.003 inch (0.1mm) thick manufacturer's standard moisture barrier.

Thickness: Nominal 1/2 inch (13mm).

Size: 1 foot tall by 1 foot wide (304x304mm) board.

Size: 1-1/2 foot tall by 2 foot wide (457x609mm) board.

Size: 2 foot tall by 2 foot wide (609x609mm) board.

Size: 2 foot tall by 3 foot wide (609x914mm) board.

Size: 2 foot tall by 4 foot wide (609x1219mm) board.

Size: 3 foot tall by 4 foot wide (914x1219mm) board.

** NOTE TO SPECIFIER **  Select Board Size.  All panels above 12 feet in length are fabricated of two or more panels with mullion strips.  Custom and small board sizes available; Insert size if not listed.  Delete eight of the next nine paragraphs.

Size: 4 foot tall by 4 foot wide (1219x1219mm) board.

Size: 4 foot tall by 5 foot wide (1219x1560mm) board.

Size: 4 foot tall by 6 foot wide (1219x1829mm) board.

Size: 4 foot tall by 8 foot wide (1219x2438mm) board.

Size: 4 foot tall by 10 foot wide (1219x3048mm) board.

Size: 4 foot tall by 12 foot wide (1219x3658mm) board.

Size: 4 foot tall by 16 foot wide (1219x4877mm) board.

Size: 4 foot tall by 20 foot wide (1219x6096mm) board.

Size: 4 foot tall by 24 foot wide (1219x7315mm) board.

Size: ___ foot tall by ___ foot wide (______ x ______mm) board.

Assembly: All boards are one piece up to 12 feet (3658mm) in length. When length exceeds 12 feet (3658mm), manufacturer's H-Channel will be provided. Assembly required at site.

Non-Magnetic Dry Erase Board: Balanced, high-pressure, factory-laminated dry erase board assembly of 3-ply construction consisting of backing sheet, core material, and a laminated hardboard face sheet with durable gloss finish highly resistant to ghosting and staining.

Face Sheet: Laminated 1/8 inch (3mm) thick hardboard.

Color: White.

Core Material: 3/8 inch (9.5mm) thick hexacomb material.

Backing Sheet: 0.003 inch (0.1mm) thick manufacturer's standard moisture barrier.

Thickness: Nominal 1/2 inch (13mm).

** NOTE TO SPECIFIER **  Select Board Size.  All panels above 12 feet in length are fabricated of two or more panels with mullion strips.  Custom and small board sizes available; Insert size if not listed.  Delete eight of the next nine paragraphs.

Size: 1 foot tall by 1 foot wide (304x304mm) board.

Size: 1-1/2 foot tall by 2 foot wide (457x609mm) board.

Size: 2 foot tall by 2 foot wide (609x609mm) board.

Size: 2 foot tall by 3 foot wide (609x914mm) board.

Size: 2 foot tall by 4 foot wide (609x1219mm) board.

Size: 3 foot tall by 4 foot wide (914x1219mm) board.

** NOTE TO SPECIFIER **  Select Board Size.  All panels above 12 feet in length are fabricated of two or more panels with mullion strips.  Custom and small board sizes available; Insert size if not listed.  Delete eight of the next nine paragraphs.

Size: 4 foot tall by 4 foot wide (1219x1219mm) board.

Size: 4 foot tall by 5 foot wide (1219x1560mm) board.

Size: 4 foot tall by 6 foot wide (1219x1829mm) board.

Size: 4 foot tall by 8 foot wide (1219x2438mm) board.

Size: 4 foot tall by 10 foot wide (1219x3048mm) board.

Size: 4 foot tall by 12 foot wide (1219x3658mm) board.

Size: 4 foot tall by 16 foot wide (1219x4877mm) board.

Size: 4 foot tall by 20 foot wide (1219x6096mm) board.

Size: 4 foot tall by 24 foot wide (1219x7315mm) board.

Size: ___ foot tall by ___ foot wide (______ x ______mm) board.

Assembly: All boards are one piece up to 12 feet (3658mm) in length. When length          exceeds 12 feet (3658mm), manufacturer's H-Channel will be provided. Assembly required at site.

** NOTE TO SPECIFIER ** Delete the next paragraph if Dry Erase Board Resurfacing Panels are not required.

Laminated Steel Resurfacing Panel: A laminated steel face sheet with a durable gloss finish highly resistant to ghosting and staining.

Face Sheet: Laminated 24 gauge steel sheet.

Color: White.

Mounting Adhesive: Manufacturer's standard pre-applied pressure sensitive       adhesive.

** NOTE TO SPECIFIER **  Select Board Size.  All panels above 12 feet in length are fabricated of two or more panels with mullion strips.  Custom and small board sizes available; Insert size if not listed.  Delete nine of the next ten paragraphs.

Size: 1 foot tall by 1 foot wide (304x304mm) board.

Size: 1-1/2 foot tall by 2 foot wide (457x609mm) board.

Size: 2 foot tall by 2 foot wide (609x609mm) board.

Size: 2 foot tall by 3 foot wide (609x914mm) board.

Size: 2 foot tall by 4 foot wide (609x1219mm) board.

Size: 3 foot tall by 4 foot wide (914x1219mm) board.

** NOTE TO SPECIFIER **  Select Board Size.  All panels above 12 feet in length are fabricated of two or more panels with mullion strips.  Custom and small board sizes available; Insert size if not listed.  Delete eight of the next nine paragraphs.

Size: 4 foot tall by 4 foot wide (1219x1219mm) board.

Size: 4 foot tall by 5 foot wide (1219x1560mm) board.

Size: 4 foot tall by 6 foot wide (1219x1829mm) board.

Size: 4 foot tall by 8 foot wide (1219x2438mm) board.

Size: 4 foot tall by 10 foot wide (1219x3048mm) board.

Size: 4 foot tall by 12 foot wide (1219x3658mm) board.

Size: 4 foot tall by 16 foot wide (1219x4877mm) board.

Size: 4 foot tall by 20 foot wide (1219x6096mm) board.

Size: 4 foot tall by 24 foot wide (1219x7315mm) board.

Size: ___ foot tall by ___ foot wide (______ x ______mm) board.

Assembly: All boards are one piece up to 12 feet (3658mm) in length. When length exceeds 12 feet (3658mm), manufacturer's seam strip will be provided. Installation required at site.

Ultimatte Magnetic Dry Erase Board: Balanced, high-pressure, factory-laminated dry erase board assembly of 3-ply construction consisting of backing sheet, core material, and a laminated 24-gauge steel face sheet with durable matte finish highly resistant to ghosting and staining.  Can be used as a projection surface as well as a whiteboard.

Face Sheet: Laminated 24 gauge steel sheet.

Color: White.

Core Material: 1/2 inch (12mm) thick hexacomb material.

Backing Sheet: 0.003 inch (0.1mm) thick manufacturer's standard moisture barrier.

Thickness: Nominal 1/2 inch (13mm).

Size: 1 foot tall by 1 foot wide (304x304mm) board.

Size: 1-1/2 foot tall by 2 foot wide (457x609mm) board.

Size: 2 foot tall by 2 foot wide (609x609mm) board.

Size: 2 foot tall by 3 foot wide (609x914mm) board.

Size: 2 foot tall by 4 foot wide (609x1219mm) board.

Size: 3 foot tall by 4 foot wide (914x1219mm) board.

** NOTE TO SPECIFIER **  Select Board Size.  All panels above 12 feet in length are fabricated of two or more panels with mullion strips.  Custom and small board sizes available; Insert size if not listed.  Delete eight of the next nine paragraphs.

Size: 4 foot tall by 4 foot wide (1219x1219mm) board.

Size: 4 foot tall by 5 foot wide (1219x1560mm) board.

Size: 4 foot tall by 6 foot wide (1219x1829mm) board.

Size: 4 foot tall by 8 foot wide (1219x2438mm) board.

Size: 4 foot tall by 10 foot wide (1219x3048mm) board.

Size: 4 foot tall by 12 foot wide (1219x3658mm) board.

Size: 4 foot tall by 16 foot wide (1219x4877mm) board.

Size: 4 foot tall by 20 foot wide (1219x6096mm) board.

Size: 4 foot tall by 24 foot wide (1219x7315mm) board.

Size: 5 foot tall by 6 foot wide (1524x1829mm) board.

Size: 5 foot tall by 8 foot wide (1524x2438mm) board.

Size: 5 foot tall by 10 foot wide (1524x3048mm) board.

Size: 5 foot tall by12 foot wide (1524x3658mm) board.

Size: ___ foot tall by ___ foot wide (______ x ______mm) board.

Assembly: All boards are one piece up to 12 feet (3658mm) in length. When length exceeds 12 feet (3658mm), manufacturer's H-Channel will be provided. Assembly required at site.

Ultimatte Laminated Steel Resurfacing Panel: A laminated steel face sheet with a durable matte finish highly resistant to ghosting and staining.  Can be used as a projection surface as well as a whiteboard.

Face Sheet: Laminated 24 gauge steel sheet.

Color: White.

Mounting Adhesive: Manufacturer's standard pre-applied pressure sensitive       adhesive.

** NOTE TO SPECIFIER **  Select Board Size.  All panels above 12 feet in length are fabricated of two or more panels with mullion strips.  Custom and small board sizes available; Insert size if not listed.  Delete nine of the next ten paragraphs.

Size: 1 foot tall by 1 foot wide (304x304mm) board.

Size: 1-1/2 foot tall by 2 foot wide (457x609mm) board.

Size: 2 foot tall by 2 foot wide (609x609mm) board.

Size: 2 foot tall by 3 foot wide (609x914mm) board.

Size: 2 foot tall by 4 foot wide (609x1219mm) board.

Size: 3 foot tall by 4 foot wide (914x1219mm) board.

** NOTE TO SPECIFIER **  Select Board Size.  All panels above 12 feet in length are fabricated of two or more panels with mullion strips.  Custom and small board sizes available; Insert size if not listed.  Delete eight of the next nine paragraphs.

Size: 4 foot tall by 4 foot wide (1219x1219mm) board.

Size: 4 foot tall by 5 foot wide (1219x1560mm) board.

Size: 4 foot tall by 6 foot wide (1219x1829mm) board.

Size: 4 foot tall by 8 foot wide (1219x2438mm) board.

Size: 4 foot tall by 10 foot wide (1219x3048mm) board.

Size: 4 foot tall by 12 foot wide (1219x3658mm) board.

Size: 4 foot tall by 16 foot wide (1219x4877mm) board.

Size: 4 foot tall by 20 foot wide (1219x6096mm) board.

Size: 4 foot tall by 24 foot wide (1219x7315mm) board.

Size: 5 foot tall by 6 foot wide (1524x1829mm) board.

Size: 5 foot tall by 8 foot wide (1524x2438mm) board.

Size: 5 foot tall by 10 foot wide (1524x3048mm) board.

Size: 5 foot tall by12 foot wide (1524x3658mm) board.

Size: ___ foot tall by ___ foot wide (______ x ______mm) board.

Assembly: All boards are one piece up to 12 feet (3658mm) in length. When length exceeds 12 feet (3658mm), manufacturer's seam strip will be provided. Installation required at site.

** NOTE TO SPECIFIER ** Delete the next paragraph if Cork Bulletin Boards are not required.

Cork Bulletin Board: Self healing tack assembly composed of natural cork sheet factory                     laminated to a hardboard backing.

Face Sheet: Laminated 1/4 inch (6mm) thick natural cork sheet.

Backing Sheet: 3/8 inch (10mm) thick hardboard.

** NOTE TO SPECIFIER **  Select Board Size.  Custom and small board sizes available; Insert size if not listed.  Delete five of the next six paragraphs.

Size: 1 foot tall by 1 foot wide (304x304mm) board.

Size: 1-1/2 foot tall by 2 foot wide (457x609mm) board.

Size: 2 foot tall by 2 foot wide (609x609mm) board.

Size: 2 foot tall by 3 foot wide (609x914mm) board.

Size: 2 foot tall by 4 foot wide (609x1219mm) board.

Size: 3 foot tall by 4 foot wide (914x1219mm) board.

** NOTE TO SPECIFIER **  Select Board Size.  All panels above 12 feet in length are fabricated of two or more panels with mullion strips.  Custom and small board sizes available; Insert size if not listed.  Delete eight of the next nine paragraphs.

Size: 4 foot tall by 4 foot wide (1219x1219mm) board.

Size: 4 foot tall by 5 foot wide (1219x1560mm) board.

Size: 4 foot tall by 6 foot wide (1219x1829mm) board.

Size: 4 foot tall by 8 foot wide (1219x2438mm) board.

Size: 4 foot tall by 10 foot wide (1219x3048mm) board.

Size: 4 foot tall by 12 foot wide (1219x3658mm) board.

Size: 4 foot tall by 16 foot wide (1219x4877mm) board.

Size: 4 foot tall by 20 foot wide (1219x6096mm) board.

Size: 4 foot tall by 24 foot wide (1219x7315mm) board.

Size: ___ foot tall by ___ foot wide (______ x ______mm) board.

** NOTE TO SPECIFIER ** Delete the next paragraph if Vinyl Bulletin Boards are not required.

** NOTE TO SPECIFIER **  Delete the entire next article if Each Visual Display board contains only one surface type.

BOARD CONFIGURATION

Combination Board Style A: Two Panels - Vertical H-Channel.

** NOTE TO SPECIFIER **  Select Total Board Size.  Delete five of the next six paragraphs.

Size: 1 foot tall by 1 foot wide (304x304mm) board.

Size: 1-1/2 foot tall by 2 foot wide (457x609mm) board.

Size: 2 foot tall by 2 foot wide (609x609mm) board.

Size: 2 foot tall by 3 foot wide (609x914mm) board.

Size: 2 foot tall by 4 foot wide (609x1219mm) board.

Size: 3 foot tall by 4 foot wide (914x1219mm) board.

** NOTE TO SPECIFIER **  Select Board Size.  All panels above 12 feet in length are fabricated of two or more panels with mullion strips.  Custom and small board sizes available; Insert size if not listed.  Delete eight of the next nine paragraphs.

Size: 4 foot tall by 4 foot wide (1219x1219mm) board.

Size: 4 foot tall by 5 foot wide (1219x1560mm) board.

Size: 4 foot tall by 6 foot wide (1219x1829mm) board.

Size: 4 foot tall by 8 foot wide (1219x2438mm) board.

Size: 4 foot tall by 10 foot wide (1219x3048mm) board.

Size: 4 foot tall by 12 foot wide (1219x3658mm) board.

Size: 4 foot tall by 16 foot wide (1219x4877mm) board.

Size: 4 foot tall by 20 foot wide (1219x6096mm) board.

Size: 4 foot tall by 24 foot wide (1219x7315mm) board.

Placement:

** NOTE TO SPECIFIER ** Select Left Side Board.  Delete two of the next three paragraphs.

Left Side: Cork Bulletin Board.

Left Side: Dry Erase Board.

** NOTE TO SPECIFIER ** Select Right Side Board.  Delete two of the next three paragraphs.

Right Side: Cork Bulletin Board.

Right Side: Dry Erase Board.

** NOTE TO SPECIFIER ** Select Bulletin Board Width.  4 foot width only available with boards 8 feet wide and larger.  Delete one of the next two paragraphs.

Combination Board Style B: Three Panels - Dual Vertical H-Channels.

Size: 3 foot tall by 3 foot wide (914x914mm) board.

Size: 4 foot tall by 4 foot wide (1219x1219mm) board.

Size: 4 foot tall by 6 foot wide (1219x1829mm) board

** NOTE TO SPECIFIER **  Select Total Board Size.  Delete three of the next four paragraphs.

Size: 4 foot tall by 8 foot wide (1219x2438mm) board.

Size: 4 foot tall by 10 foot wide (1219x3048mm) board.

Size: 4 foot tall by 12 foot wide (1219x3658mm) board.

Size: 4 foot tall by 16 foot wide (1219x4877mm) board.

Size: 4 foot tall by 20 foot wide (1219x6096mm) board.

Size: 4 foot tall by 24 foot wide (1219x7315mm) board.

Placement:

** NOTE TO SPECIFIER ** Select Left Side Board.  Delete two of the next three paragraphs.

        - Left Side: Cork Bulletin Board.

Center: Dry Erase Board.

** NOTE TO SPECIFIER ** Select Right Side Board.  Delete one of the next two paragraphs.

Right Side: Cork Bulletin Board.

** NOTE TO SPECIFIER ** Select Bulletin Board Width.  4 foot width only available with boards 16 feet wide.  Delete one of the next two paragraphs.

Combination Board Style C: 2 Panels – H-Channel, Overhead Bulletin Board.

** NOTE TO SPECIFIER **  Select Total Board Size.  Custom and small board sizes available; Insert size if not listed.  Delete six of the next seven paragraphs.

Size: 2 foot tall by 2 foot wide (609x609mm) board.

Size: 3 foot tall by 3 foot wide (914x914mm) board.

Size: 4 foot tall by 4 foot wide (1219x1219mm) board.

Size: 4 foot tall by 6 foot wide (1219x1829mm) board

** NOTE TO SPECIFIER **  Select Total Board Size.  Delete three of the next four paragraphs.

Size: 4 foot tall by 8 foot wide (1219x2438mm) board.

Size: 4 foot tall by 10 foot wide (1219x3048mm) board.

Size: 4 foot tall by 12 foot wide (1219x3658mm) board.

Size: 4 foot tall by 16 foot wide (1219x4877mm) board.

Size: 4 foot tall by 20 foot wide (1219x6096mm) board.

Size: 4 foot tall by 24 foot wide (1219x7315mm) board.

Size: ___ foot tall by ___ foot wide (______ x ______mm) board.

Placement:

** NOTE TO SPECIFIER ** Select Bulletin Board.  Delete one of the next two paragraphs.

Upper: Cork Bulletin Board.

Lower: Dry Erase Board.

** NOTE TO SPECIFIER **  Select Mullion Type.  Map rail is standard.  Delete one of the next two paragraphs.

H-Channel

Combination Board Style D: 4 Panels - Dual Vertical H-Channels, Horizontal H-Channel, and Overhead Bulletin Board.

Size: 4 foot tall by 4 foot wide (1219x1219mm) board.

Size: 4 foot tall by 6 foot wide (1219x1829mm) board

** NOTE TO SPECIFIER **  Select Total Board Size.  Custom and small board sizes available; Insert size if not listed.  Delete four of the next five paragraphs.

Size: 4 foot tall by 8 foot wide (1219x2438mm) board.

Size: 4 foot tall by 10 foot wide (1219x3048mm) board.

Size: 4 foot tall by 12 foot wide (1219x3658mm) board.

Size: 4 foot tall by 16 foot wide (1219x4877mm) board.

Size: 4 foot tall by 20 foot wide (1219x6096mm) board.

Size: 4 foot tall by 24 foot wide (1219x7315mm) board.

Size: ___ foot tall by ___ foot wide (______ x ______mm) board.

Placement:

** NOTE TO SPECIFIER ** Select Upper Board.  Delete two of the next three paragraphs.

Upper: Cork Bulletin Board.

** NOTE TO SPECIFIER ** Select Left Side Board.  Delete two of the next three paragraphs.

Left Side: Cork Bulletin Board.

Center: Dry Erase Board.

** NOTE TO SPECIFIER ** Select Right Side Board.  Delete one of the next two paragraphs.

Right Side: Cork Bulletin Board.

H-Channels.

** NOTE TO SPECIFIER ** Select Bulletin Board Width.  4 foot width only available with boards 16 feet wide.  Delete one of the next two paragraphs.

** NOTE TO SPECIFIER **  Select Mullion Type.  Map rail is standard.  Delete paragraphs not required.

** NOTE TO SPECIFIER **  Delete the entire next paragraph if no Special Purpose Graphics are required.  Where multiple boards are specified, coordinate with Contract Drawings and/or Visual Board Schedules.

Standard Graphic Boards: Graphics permanently laminated into dry erase board.

** NOTE TO SPECIFIER **  Select Specialty graphic(s) from the next six paragraphs. Custom Graphics are available upon request.  Delete all graphics not required.

Graphic: Penmanship lines.

Graphic: Music staff lines.

Graphic: 1 inch (25mm) square grid lines.

Graphic: EZ Grid, Grid 1”

Graphic: EZ Grid, Grid 2”

Graphic: EZ Grid, Dot 1”

Graphic: EZ Grid, Dot 2”

Graphic: EZ Grid, ISO 1”

Graphic: EZ Grid, ISO 2”

Graphic: Standard Sport, Basketball

Graphic: Standard Sport, Hockey

Graphic: Standard Sport, Football

Graphic: Standard Sport, Soccer

Graphic: Standard Sport, Volleyball

Graphic: Calendars, 1, 2, 3, 4, 6 & 12 months and 1 month plus

Placement: Covering entire dry erase board.

Size: 1 foot tall by 1 foot wide (304x304mm) board.

Size: 1-1/2 foot tall by 2 foot wide (457x609mm) board.

Size: 2 foot tall by 2 foot wide (609x609mm) board.

Size: 2 foot tall by 3 foot wide (609x914mm) board.

Size: 2 foot tall by 4 foot wide (609x1219mm) board.

Size: 3 foot tall by 4 foot wide (914x1219mm) board.

** NOTE TO SPECIFIER **  Select Total Board Size.  Custom and small board sizes available; Insert size if not listed.  Delete six of the next seven paragraphs.

Size: 4 foot tall by 4 foot wide (1219x1219mm) board.

Size: 4 foot tall by 5 foot wide (1219x1560mm) board.

Size: 4 foot tall by 6 foot wide (1219x1829mm) board.

Size: 4 foot tall by 8 foot wide (1219x2438mm) board.

Size: 4 foot tall by 10 foot wide (1219x3048mm) board.

Size: 4 foot tall by 12 foot wide (1219x3658mm) board.

Graphic Combination Boards: 4 foot by 4 foot (1219mm x 1219mm) graphic permanently laminated onto one side of the dry erase board. Remaining surface of the board remains plain.

** NOTE TO SPECIFIER **  Select Specialty graphic(s) from the next six paragraphs. Custom Graphics are available upon request.  Delete all graphics not required.

Graphic: Penmanship lines.

Graphic: Music staff lines.

Graphic: 1 inch (25mm) square grid lines.

Graphic: EZ Grid, Grid 1”

Graphic: EZ Grid, Grid 2”

Graphic: EZ Grid, Dot 1”

Graphic: EZ Grid, Dot 2”

Graphic: EZ Grid, ISO 1”

Graphic: EZ Grid, ISO 2”

Graphic: Standard Sport, Basketball

Graphic: Standard Sport, Hockey

Graphic: Standard Sport, Football

Graphic: Standard Sport, Soccer

Graphic: Standard Sport, Volleyball

Graphic: Calendars, 1, 2, 3, 4, 6 & 12 months and 1 month plus

Graphic: _________________

Size Restrictions: All graphics can be ordered in all available sizes.

** NOTE TO SPECIFIER **  Select graphic placement.  Delete one of the next two paragraphs.

** NOTE TO SPECIFIER **  Select Total Board Size.  Custom and small board sizes available; Insert size if not listed.  Delete six of the next seven paragraphs.

Size: 4 foot tall by 4 foot wide (1219x1219mm) board.

Size: 4 foot tall by 5 foot wide (1219x1560mm) board.

Size: 4 foot tall by 6 foot wide (1219x1829mm) board.

Size: 4 foot tall by 8 foot wide (1219x2438mm) board.

Size: 4 foot tall by 10 foot wide (1219x3048mm) board.

Size: 4 foot tall by 12 foot wide (1219x3658mm) board.

Size: 4 foot tall by 16 foot wide (1219x4877mm) board.

Size: ___ foot tall by ___ foot wide (______ x ______mm) board.

Assembly: All boards are one piece up to 12 feet (3658mm) in length. When length exceeds 12 feet (3658mm), manufacturer's H-Channel will be provided. Assembly required at site.

** NOTE TO SPECIFIER **  Retain only frame required for this project.  Delete the next paragraph if no frame is specified.

FRAMING

** NOTE TO SPECIFIER **  Select Frame Type.  Delete one of the next two paragraphs or both if no Frame is specified.  Modify the included text as instructed.

Aluminum Frame and Marker Tray:

Thickness:   .719 inch (18mm) thick, extruded aluminum frame.

** NOTE TO SPECIFIER **  Select Width. Delete one of the next two paragraphs.

Width: Narrow - 5/8 inch (15mm).

Width: Wide – 1 1/8 inch (29mm).

Marker Tray: 2 5/8 inch (67mm) Continuous solid extruded aluminum tray with 3 channels and protective plastic end caps.

Finish: Satin Anodized clear finish.

End Cap Color: Silver.

Wood Frame and Marker Tray:

Thickness: 0.875 inch (22mm) thick, solid wood frame.

** NOTE TO SPECIFIER **  Select Width. Delete one of the next two paragraphs.

Width: Narrow – 1 1/4 inch (32mm).

Width: Wide – 2 1/4 inch (57mm).

Marker Tray: 2 1/4 inch (64mm) deep single channel tray.

** NOTE TO SPECIFIER **  Select Wood Trim Type. Delete three of the next four paragraphs.

Wood Type: Natural Oak.

Wood Type: Maple.

Wood Type: Maple with Mahogany Stain.

Wood Type: Maple with Cherry Stain.

Wood Type: Maple with Black Paint.

ACCESSORIES

** NOTE TO SPECIFIER ** Delete the next paragraph if no Map Rail is specified.  Retain only included accessories required for this project.

Map Rail: Standard 1 inch (25mm) map rail with cork insert.

Map Hooks and Clips: Extruded Aluminum.

Flag Holder: Extruded Aluminum.

Map Winders: Extruded Aluminum.

** NOTE TO SPECIFIER ** Delete the next paragraph if markers and cloths are not specified.

Markers and Cleaning Cloths:

Dry Erase Marker Set including red, blue, green and black.

EverCloth - Reusable dry erase marking board cleaning cloth.

EXECUTION

EXAMINATION AND PREPARATION

Do not begin installation until substrates have been properly prepared.

If substrate preparation is the responsibility of another installer, notify Architect of unsatisfactory preparation before proceeding.

Clean surfaces thoroughly after installation with water or glass cleaner.

INSTALLATION

Install in accordance with manufacturer's instructions.

Install all units in locations shown on plans, at mounting heights specified on the Contract Drawings. Keep perimeter lines straight, plumb and level.

EverWhite products are designed to be installation-ready, however, installation and the installation environment are out of EverWhite’s control and therefore installation is not warranted by EverWhite in any circumstance.

CLEANING AND PROTECTION

Clean display boards prior to project closeout.

Protect installed products until completion of project.

Repair or replace damaged products before Substantial Completion.

END OF SECTION